## Slide 1
Intelligent Robotics Lab
Development of a SLAM and Autonomous Navigation System for a Self-Driving Car
Student: Amit Sajeev
Supervisor: Prof. Dr. Dmitrii Dobriborsci
Deadline: September 14, 2026
Notes: 1

## Slide 2
Problem definition
2
Develop a SLAM and Autonomous Navigation System for a Self-Driving Car
  ROS2-based autonomous navigation system for the Quanser QCar by integrating sensor fusion
Problem statement
  Building a complete stack for a self driving car
  To fuse different sensor data into the environment to localize and navigate the car in real time.
  Design architecture for ROS2 and implement SLAM
Scope
  Deliverables: ROS2 Humble simulation environment, QCar URDF model, ros2_control joint controllers, RViz visualization, documented repository
Notes: 2

## Slide 3
Thesis goal
3
Main objective
Design and implement a ROS2-based perception and navigation system for the Quanser QCar, enabling real-time SLAM, localization and autonomous indoor driving.
Sub-objectives
Sensor characterization and time-synchronized data acquisition (LiDAR, IMU, encoders, camera)
Multi-sensor fusion for state estimation using EKF/UKF (robot_localization package)
Evaluate and configure ROS2-compatible SLAM algorithms (Cartographer, KISS-ICP, gmapping)
Integrate Nav2 for autonomous path planning and obstacle avoidance on the QCar
Notes: 3

## Slide 4
Plan
4
Plan for the last 2 weeks
Expected tasks
  T1: Resolve corner-cutting/curve-radius complaint
  T2: Connect to physical QCar, establish ROS2 communication
  T3: Deploy simulation stack to QCar onboard computer
  T4: Check LiDAR sensor on real hardware
  T5: Test keyboard teleop on real QCar
Connection to the milestones:
  M7: Simulation stack complete; hardware integration initiated
Notes: 4

## Slide 5
Progress
5
Work completed
Completed tasks
  T1: Improved goal accuracy - increased minimum turning radius and loosened yaw tolerance; robot now reaches goals almost accurately
  T2: Investigated remaining path deviation on tight-turn goals - tested 5 parameters, no single fix found; confirmed it's a geometry limitation of the goal itself, not a software bug
  T3: Created qcar_hardware package - reference docs, hardware test scripts and integration guide for the physical Qcar
  T4: Solved ROS2 version conflict - QCar runs Dashing, dev PC runs Humble; set up a separate native Dashing workspace on the QCar to avoid compatibility issues
  T5: First successful hardware run - physical QCar connected and driven via keyboard teleop
  Progress: Nav2 setup with Smac global planner + MPPI sampling-based local controller. Issues resolved. Harware integration completed and successfully teleoperated the robot.
Work NOT completed
Real LiDAR, encoder odometry and stack integration on hardware
SLAM on real hardware - not yet run
Humble-tuned Nav2/MPPI stack can't run natively on QCar's Dashing workspace
Planned resolution: Docker to run Humble-based navigation stack in a container on the QCar, alongside native Dashing workspace handling direct hardware I/O
Notes: 5

## Slide 6
Plan for the next 2 weeks
6
Upcoming tasks:
T1: Set up Docker to run Humble-based Nav2/MPPI stack on/against the QCar
T2: Expand on-device Dashing workspace - real LiDAR node, encoder odometry
T3: Validate teleop more thoroughly - drive/steering response under real load and friction
T4: Run Cartographer/SLAM on real hardware for physical-environment map
T5: Begin end-to-end testing of Nav2 autonomy stack on hardware via Docker
Expected outcomes:
Successfully able to navigate in physical-environment with QCar
Milestone:
M7: Humble navigation stack running on the physical QCar via Docker; real sensor integration underway
Notes: 6

## Slide 7
Results: QCar Hardware Teleoperation
https://www.youtube.com/watch?v=KhUEylLyjYM

## Slide 8
Issues faced
At times take multiple iterations to reroute
Robot deviates from Nav2 planned curved path.

## Slide 9
Herzlichen Dank für Ihr Interesse!
Prof. Dr. Dmitrii Dobriborsci
Dmitrii.dobriborsci@th-deg.de
Technologie
Campus Cham
Badstraße 21
93413 Cham
www.tc-cham.de
KONTAKT
9