## Slide 1
Intelligent Robotics Lab
Development of a SLAM and Autonomous Navigation System for a Self-Driving Car
Student: Amit Sajeev
Supervisor: Prof. Dr. Dmitrii Dobriborsci
Deadline: September 14, 2026
Notes: 1

## Slide 2
Problem definition
2
Develop a SLAM and Autonomous Navigation System for a Self-Driving Car
  ROS2-based autonomous navigation system for the Quanser QCar by integrating sensor fusion
Problem statement
  Building a complete stack for a self driving car
  To fuse different sensor data into the environment to localize and navigate the car in real time.
  Design architecture for ROS2 and implement SLAM
Scope
  Deliverables: ROS2 Humble simulation environment, QCar URDF model, ros2_control joint controllers, RViz visualization, documented repository
Notes: 2

## Slide 3
Thesis goal
3
Main objective
Design and implement a ROS2-based perception and navigation system for the Quanser QCar, enabling real-time SLAM, localization and autonomous indoor driving.
Sub-objectives
Sensor characterization and time-synchronized data acquisition (LiDAR, IMU, encoders, camera)
Multi-sensor fusion for state estimation using EKF/UKF (robot_localization package)
Evaluate and configure ROS2-compatible SLAM algorithms (Cartographer, KISS-ICP, gmapping)
Integrate Nav2 for autonomous path planning and obstacle avoidance on the QCar
Notes: 3

## Slide 4
Plan
4
Plan for the last 2 weeks
Expected tasks
  T1: Fix navigation inaccuracy
  T2: Replace hand-rolled converter with ackermann_steering_controller (ros2_control)
  T3: Switch to gazebo_ros_ackermann_drive plugin for native Ackermann kinematics + odometry
  T4: Fix wheel collision geometry and friction for correct physics
  T5: Tune Nav2 planner and controller for Ackermann vehicle
  T6: Begin hardware integration
Connection to the milestones:
  M6: Kinematically correct Ackermann simulation stack
Notes: 4

## Slide 5
Progress
5
Work completed
Completed tasks
  T1: Replaced cmd_vel_to_drive.py + dual joint controllers with ackermann_steering_controller
  T2: Replaced ackermann_steering_controller with gazebo_ros_ackermann_drive plugin - simpler architecture, native /odom and TF publishing, no relay nodes
  T3: Fixed three physics bugs exposed by plugin: wheel collision meshes (plugin couldn't read radius → robot couldn't move), zero wheel friction, steering PID gains too weak
  T4: Restructured the behavior tree
  T5: Switched global planner from NavFn (Dijkstra) to Smac - heading-aware planning with K-turn/reversal support; resolved root cause of goal-approach oscillation
  T6: Replaced local controller from Regulated Pure Pursuit to MPPI
  T7: Fixed MPPI collision checking - was checking robot center only, not actual rectangular car frame
  T8: Fixed enforce_path_inversion flag - MPPI was not handling planned reversal segments correctly
  T9: Tuned AMCL for localization jitter - ruled out vehicle physics as cause of remaining failures
  T10: Removed PreferForwardCritic as it was directly fighting the planner's own decisions
  T11: Fixed turns early into curve - two separate critics targeting look-ahead points past the curve start
Notes: 5

## Slide 6
Progress
6
Work completed
Completed tasks
  T12: Robot wasn’t moving on reorientation-only goal - fixed - three path-adherence critics measured distance to goal, switching off for entire maneuver
  T13: Robot doesn't move when path starts with a turn - fixed - planner bug inserting a pointless reversal-then-forward wiggle at path
  T14: Fixed /joint_states reporting fake frozen state - wheels appeared static in RViz while robot was moving correctly
  T15: Built custom EarlyCommitCritic MPPI critic from scratch - no existing critic provided heading guidance for immediate-curve cases; fixed mismatch between custom code and Nav2's precompiled MPPI library
  T16: Fixed 4 stacked bugs behind persistent failure: runaway 33Hz replanning (behavior tree bug), zero safety margin between planner and controller turning radius limits, and MPPI warm-start self-reinforcing stall
  Progress: Stack moved from approximated Ackermann conversion + basic Nav2 to kinematically to Smac global planner + MPPI sampling-based local controller. End-to-end navigation verified. Corner-cutting/curve-radius tuning still inconclusive.
Work NOT completed
Corner-cutting on curves - not proven fixable with single critic weight adjustment; under investigation
Hardware integration - deprioritized in favor of achieving correct simulation kinematics first
Notes: 6

## Slide 7
Plan for the next 2 weeks
7
Upcoming tasks:
T1: Resolve corner-cutting/curve-radius complaint
T2: Connect to physical QCar and establish ROS2 Humble communication
T3: Deploy simulation stack to QCar onboard computer
T4: Calibrate LiDAR sensor on real hardware - verify /scan topic publishing
T5: Test keyboard teleop on real QCar - validate drive and steering response
Expected outcomes:
Navigation stack fully tuned and verified in simulation
Hardware integration initiated - QCar teleoperated and sensor-verified
Milestone:
M6: Simulation stack complete with verified Ackermann kinematics; hardware integration initiated
Notes: 7

## Slide 8
Results: SLAM Mapping, Localization and Autonomous Navigation
https://www.youtube.com/watch?v=nIZiZn91m-E

## Slide 9
Issues faced
At times take multiple iterations to reroute
Robot deviates from Nav2 planned curved path.

## Slide 10
Herzlichen Dank für Ihr Interesse!
Prof. Dr. Dmitrii Dobriborsci
Dmitrii.dobriborsci@th-deg.de
Technologie
Campus Cham
Badstraße 21
93413 Cham
www.tc-cham.de
KONTAKT
10